## Slide 1: IVOD System Briefing

## Slide 2: In-vehicle Occupant Detection (IVOD)
Current Setup
Testing ground
Showroom
RB Pi (192.168.70.124)
- Radar app
router
IVOD server (192.168.70.120)
- 0mq and websocket server
- Web data collection server
- DBscan module
RB Pi (192.168.70.122)
- Radar app

## Slide 3: In-vehicle Occupant Detection (IVOD)
Issues
  The systems are quite standalone and implemented by previous interns
  Data visualization on React are fairly incomplete
  No spare set of uRAD for us to develop on
    Currently held by our interns for data collection

## Slide 4: Truncated System Diagram
RPi
&
uRad
RPi
&
uRad
IVOD Server
Inference Engine
Workflow
Solace
PubSub
Bus
IVOD Server
  Marshal data from lanes to inference engine
  Translate commands from workflow to components
  Return change in prediction to workflow
Inference Engine
  Make predictions based on received data from radars

## Slide 5: Data Flow - 1
RPi
&
uRad
RPi
&
uRad
IVOD Server
Inference Engine
Workflow
E1
E2
E3
E4
Raspi sends raw data to IVOD Server
  This data will be tagged in JSON with radar1 and radar2 labels

## Slide 6: Data Flow - 2
RPi
&
uRad
RPi
&
uRad
IVOD Server
Inference Engine
Workflow
E1
E2
E3
E4
IVOD server sends combined data stream to inference engine
  This data will be tagged in JSON with lane number

## Slide 7: Data Flow - 3
RPi
&
uRad
RPi
&
uRad
IVOD Server
Inference Engine
Workflow
E1
E2
E3
E4
Inference Engine returns with the prediction
  This data will update the IVOD server with the number of passengers in the car

## Slide 8: Data Flow - 4
RPi
&
uRad
RPi
&
uRad
IVOD Server
Inference Engine
Workflow
E1
E2
E3
E4
IVOD server sends update in prediction to workflow
  This will only be sent over if there is a change in the number

## Slide 9: Context

## Slide 10: Testing
IVOD Data Feed (Historical Data)
  My effort
    Software will be provided to iterate through current datasets
      Will pass you the dataset collected so far today
    This will be published to the inference engine through Solace PubSub+ Standard

## Slide 11: Testing
IVOD Data Feed (Historical Data)
  Your effort
    Install and setup Solace PubSub+ Standard on a local Docker instance
      Create the following queue after installation:
        evt/v1/ivod_server/inf_eng/training
    Train the inference engine based on the data provided by the simulator